## Slide 1: IPv4 / IPv6 Performance Measurement Panel
Geoff Huston, APNIC
February 2014

## Slide 2: The Environment
We use Google Ads to deliver test scripts to a very broad cross-section of Internet Users
  We use a script that requests dual-stack end clients to fetch unique V6 and a V4 URLs from our servers
    (servers located in the US, Germany and Australia)
  We have some 300,000 - 400,000 ads delivered per day
  We packet dump all activity on the server

## Slide 3: Connection Reliability
Looking at the TCP handshake, what proportion of IPv6 clients send us a SYN, but no following ACK?
SYN
SYN+ACK
ACK

## Slide 4: Connection Reliability

## Slide 5: Connection Reliability
IPv4 failure rate: 0.1% - 0.3%
IPv6 failure rate: 1.2 – 2.1%
This appears to indicate that a visible proportion of IPv6-capable end user devices are located behind firewall/filter setups that deny incoming IPv6 packets

## Slide 6: IPv6 Connection Failure Rate by Origin AS
AS Samples Failure Rate (%) AS Name
14210 22 95.45 EDGECAST-DCA - EdgeCast Networks, Inc. US
132497 295 78.64 DNA-AS-AP SMARTLINK BROADBAND SERVICES PVT LTD IN
55680 53 75.47 KSI-UAJY-AS-ID Kantor Sistem Informasi Universitas Atma Jaya Yogyakarta ID
198864 341 75.37 QMW-AC-UK Queen Mary and Westfield College, University of London GB
18106 45 73.33 VIEWQWEST-SG-AP Viewqwest Pte Ltd SG
25592 51 62.75 NETIS-AS NETIS TELECOM Inc. Yaroslavl region ISP provider Russia RU
2856 27 59.26 BT-UK-AS BTnet UK Regional network GB
17660 141 58.16 DRUKNET-AS DrukNet ISP BT
22773 33 57.58 ASN-CXA-ALL-CCI-22773-RDC - Cox Communications Inc. US
17705 37 51.35 INSPIRENET-AS-AP InSPire Net Ltd NZ
55947 128 46.09 BBNL-IN Bangalore Broadband Network Pvt Ltd IN
4755 175 43.43 TATACOMM-AS TATA Communications formerly VSNL is Leading ISP IN
278 45 40.00 Universidad Nacional Autonoma de Mexico MX
53187 28 35.71 UNIVERSIDADE ESTADUAL DE CAMPINAS BR
23148 108 27.78 TERREMARK Terremark US
1930 4808 25.21 RCCN Rede Ciencia Tecnologia e Sociedade (RCTS) PT
10429 60 25.00 Telefonica Data S.A. BR
17832 73 23.29 SIXNGIX-AS-KR Korea Internet Security Agency KR
45133 39 23.08 SINGAPORE-POLYTECHNIC-AS-AP Singapore Polytechnic SG
21366 50 22.00 KYMP KYMP OY FI
This table looks at the origin AS’s with more than 20 sample points – these are the
origin AS’s with the highest failure rates

## Slide 7: IPv6 Connection Failure Rate by Origin AS
AS Samples Failure Rate (%) AS Name
786 458,143 1.22 JANET JISC Collections And Janet Limited GB
15169 106,221 0.08 GOOGLE - Google Inc. US
8708 75,393 5.70 RCS-RDS RCS & RDS SA RO
7922 57,659 1.84 COMCAST-7922 - Comcast Cable Communications, Inc. US
7018 50,489 1.22 ATT-INTERNET4 - AT&T Services, Inc. US
2516 50,358 0.16 KDDI KDDI CORPORATION JP
12322 38,125 5.02 PROXAD Free SAS FR
6147 32,512 1.75 Telefonica del Peru S.A.A. PE
22394 27,237 0.34 CELLCO - Cellco Partnership DBA Verizon Wireless US
23910 23,372 2.98 CNGI-CERNET2-AS-AP China Next Generation Internet CERNET2 CN
4739 19,398 0.77 INTERNODE-AS Internode Pty Ltd AU
3303 17,319 4.45 SWISSCOM Swisscom (Switzerland) Ltd CH
4773 13,963 0.57 MOBILEONELTD-AS-AP MobileOne Ltd. Internet Service Provider Singapore SG
19782 8,172 0.06 INDIANAGIGAPOP - Indiana University US
7575 7,863 3.84 AARNET-AS-AP Australian Academic and Reasearch Network (AARNet) AU
This table looks at the origin AS’s where we have the highest number of samples

## Slide 8: IPv6 Connection Failure Rate for US + CA Nets
AS Samples Failure Rate (%) AS Name
14210 22 95.45 EDGECAST-DCA - EdgeCast Networks, Inc. US
22773 33 57.58 ASN-CXA-ALL-CCI-22773-RDC - Cox Communications Inc. US
23148 108 27.78 TERREMARK Terremark US
237 265 21.13 MERIT-AS-14 - Merit Network Inc. US
5707 24 20.83 UTHSC-H - The University of Texas Health Science Center at Houston US
812 1139 17.12 ROGERS-CABLE - Rogers Cable Communications Inc. CA
11351 471 15.50 RR-NYSREGION-ASN-01 - Time Warner Cable Internet LLC US
2055 325 14.46 LSU-1 - Louisiana State University US
174 25 12.00 COGENT Cogent/PSI US
12271 1850 11.24 SCRR-12271 - Time Warner Cable Internet LLC US
11426 209 9.09 SCRR-11426 - Time Warner Cable Internet LLC US
1312 527 8.54 VA-TECH-AS - Virginia Polytechnic Institute and State Univ. US
10796 669 7.77 SCRR-10796 - Time Warner Cable Internet LLC US
1280 97 6.19 ISC-AS1280 Internet Systems Consortium, Inc. US
11427 2102 4.52 SCRR-11427 - Time Warner Cable Internet LLC US
3356 316 4.43 LEVEL3 Level 3 Communications US
12222 24 4.17 AS12222 Akamai Technologies US
20001 4505 3.26 ROADRUNNER-WEST - Time Warner Cable Internet LLC US
6939 4592 3.11 HURRICANE - Hurricane Electric, Inc. US
33522 37 2.70 CPANEL-INC - cPanel, Inc. US

## Slide 9: RTT Measurements
Data performance is highly dependent on the RTT across the data connection
Is IPv6 faster or slower than IPv4 in terms of an RTT comparison?

## Slide 10: RTT Estimate
Measuring the time interval for the completion of the TCP handshake
SYN
SYN+ACK
ACK
RTT Interval

## Slide 11: Paired RTT Distribution
Take the TCP handshake and measure the elapsed time at the server between the initial SYN and the following ACK packet
  this time value is an indicator of the RTT
Take the measurements where we have web log evidence that the IPv4 and IPv6 addresses correspond to a single experiment, and generate a ratio of the two RTT values

## Slide 12: Paired RTT Distribution
IPv6 is faster than IPv4
IPv4 is faster than IPv6
Then:
July 2012
% of RTT measurements
3x
3x
2x
2x
1.5x
1.5x
=
RTT Ratio

## Slide 13: Paired RTT Distribution
IPv6 is faster than IPv4
IPv4 is faster than IPv6
Then:
July 2012
Now:
December 2013
% of RTT measurements
3x
3x
2x
2x
1.5x
1.5x
=
RTT Ratio

## Slide 14: RTT Distribution
There is a slight change in the RTT distributions over the past 12 months favoring IPv6 being slightly faster than IPv4
  This could be due to different network paths between IPv4 and IPv6
  Or less deployment of port 80 trapping middleware in IPv6 as compared to IPv4