## Slide 1: DNS over IPv6 - A Study in Fragmentation
DNS OARC, September 2017
Geoff Huston, Joao Damas
APNIC Labs

## Slide 2: What happens to a “large” DNS response?
(Where “large” is > 1280 octets)

## Slide 3: What happens to a “large” DNS response?
(Where “large” is > 1280 octets)
For example:
  What happens in a signed DNSSEC response when there are multiple RRSIG records?

## Slide 4: What happens to a “large” DNS response?
$ dig +dnssec DNSKEY org
; <<>> DiG 9.8.3-P1 <<>> +dnssec DNSKEY org
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 21353
;; flags: qr rd ra ad; QUERY: 1, ANSWER: 7, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags: do; udp: 512;
; QUESTION SECTION:
;org. IN DNSKEY
;; ANSWER SECTION:
org. 861 IN DNSKEY 256 3 7 AwEAAXxsMmN/JgpEE9Y4uFNRJm7Q9GBwmEYUCsCxuKlg
org. 861 IN DNSKEY 256 3 7 AwEAAayiVbuM+ehlsKsuAL1CI3mA+5JM7ti3VeY8ysmo
org. 861 IN DNSKEY 257 3 7 AwEAAZTjbIO5kIpxWUtyXc8avsKyHIIZ+LjC2Dv8naO+
org. 861 IN DNSKEY 257 3 7 AwEAAcMnWBKLuvG/LwnPVykcmpvnntwxfshHlHRhlY0F
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 3947
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 9795
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 17883
;; Query time: 134 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Mon Jul 31 12:07:16 2017
;; MSG SIZE rcvd: 1625
The response to a DNSKEY query for .org uses a response of 1,625 octets!

## Slide 5: What happens to a “large” DNS response?
(Where “large” is > 1280 octets)
For example:
The case of the upcoming key roll, when the response to a DNSKEY query will be 1,414 octets for a few weeks (and 1,425 octets at the end of the roll)?

## Slide 6: What we expect…
When a resolver offers no EDNS(0) UDP buffer size then the server offers a truncated UDP response no larger than 512 octet of DNS payload
  The resolver should be capable of interpreting this truncated response as a signal to re-query using TCP

## Slide 7: What we expect…
When resolvers offer a large UDP buffer size in the EDNS(0) query options then this denotes a capability of the resolver to process a large response – the server may then send a large UDP response which may involve UDP fragmentation
The implicit assumption in the query’s EDNS(0) buffer size offer Is that the network path is equally capable of handling large UDP responses

## Slide 8: However…
UDP Fragmentation has its problems
  UDP trailing fragments in IPv4 and IPv6 may encounter fragment filtering rules on firewalls in front of resolvers

## Slide 9: However…
UDP Fragmentation has its problems
  UDP trailing fragments in IPv4 and IPv6 may encounter fragment filtering rules on firewalls in front of resolvers
  Large UDP packets in IPv6 may encounter path MTU mismatch problems, and the ICMP6 Packet Too Big diagnostic message may be filtered.
  Even if it is delivered, the host may not process the message due to the lack of verification of the authenticity of the ICMP6 message. Because the protocol is UDP, receipt of an ICMP6 message will not cause retransmission of a re-framed packet.

## Slide 10: However…
UDP Fragmentation has its problems
  UDP trailing fragments in IPv4 and IPv6 may encounter fragment filtering rules on firewalls in front of resolvers
  Large UDP packets in IPv6 may encounter path MTU mismatch problems, and the ICMP6 Packet Too Big diagnostic message may be filtered.
  Even if it is delivered, the host may not process the message due to the lack of verification of the authenticity of the ICMP6 message. Because the protocol is UDP, receipt of an ICMP6 message will not cause retransmission of a re-framed packet.
  UDP fragments in IPv6 are implemented by Extension Headers. There is some evidence of deployment of IPv6 switching equipment that unilaterally discards IPv6 packets with extension headers (RFC 7872)

## Slide 11: For example:
$ dig +bufsize=4096 +dnssec question.dotnxdomain.net. @8.8.8.8
; <<>> DiG 9.9.5-9+deb8u10-Debian <<>> +bufsize=4096 +dnssec question.dotnxdomain.net. @8.8.8.8
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: SERVFAIL, id: 34058
;; flags: qr rd ra; QUERY: 1, ANSWER: 0, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags: do; udp: 512
;; QUESTION SECTION:
;question.ap2.dotnxdomain.net. IN A
;; Query time: 3477 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Thu Jul 06 04:57:41 UTC 2017
;; MSG SIZE rcvd: 104
The only authoritative name server for this zone is via IPv6
Yes, I’m asking Google’s public
DNS resolver service over IPv4, and getting Googles PDNS to query the authoritative server over IPv6

## Slide 12: For example:
$ dig +bufsize=4096 +dnssec question.dotnxdomain.net. @8.8.8.8
; <<>> DiG 9.9.5-9+deb8u10-Debian <<>> +bufsize=4096 +dnssec question.dotnxdomain.net. @8.8.8.8
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: SERVFAIL, id: 34058
;; flags: qr rd ra; QUERY: 1, ANSWER: 0, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags: do; udp: 512
;; QUESTION SECTION:
;question.ap2.dotnxdomain.net. IN A
;; Query time: 3477 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Thu Jul 06 04:57:41 UTC 2017
;; MSG SIZE rcvd: 104
The only authoritative name server for this zone is via IPv6
Yes, I’m asking Google’s public
DNS resolver service over IPv4, and getting Googles PDNS to query the authoritative server over IPv6
Oops!

## Slide 13: For example:
$ dig +bufsize=4096 +dnssec question.dotnxdomain.net. @8.8.8.8
; <<>> DiG 9.9.5-9+deb8u10-Debian <<>> +bufsize=4096 +dnssec question.dotnxdomain.net. @8.8.8.8
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: SERVFAIL, id: 34058
;; flags: qr rd ra; QUERY: 1, ANSWER: 0, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags: do; udp: 512
;; QUESTION SECTION:
;question.ap2.dotnxdomain.net. IN A
;; Query time: 3477 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Thu Jul 06 04:57:41 UTC 2017
;; MSG SIZE rcvd: 104
The only authoritative name server for this zone is via IPv6
Yes, I’m asking Google’s public
DNS resolver service over IPv4, and getting Googles PDNS to query the authoritative server over IPv6
Oops!
If the IPv6-only response from the authoritative name server to Google’s name server exceeds 1500 octets the Google resolver returns SERVFAIL, despite providing a large UDP Buffer size option to the authoritative name server

## Slide 14: However…
UDP Fragmentation has its problems
  UDP trailing fragments in IPv4 and IPv6 may encounter fragment filtering rules on firewalls in front of resolvers
  Large UDP packets in IPv6 may encounter path MTU mismatch problems, and the ICMP6 Packet Too Big diagnostic message may be filtered.
  Even if it is delivered, the host may not process the message due to the lack of verification of the authenticity of the ICMP6 message. Because the protocol is UDP, receipt of an ICMP6 message will not cause retransmission of a re-framed packet.
  UDP fragments in IPv6 are implemented by Extension Headers. There is some evidence of deployment of IPv6 switching equipment that unilaterally discards IPv6 packets with extension headers (RFC 7872)
DNS over TCP is not always available
  TCP over DNS may be blocked by firewall filtering rules even when the resolver re-queries using a smaller EDNS0 buffer size to generate a truncated response (*)
* http://www.potaroo.net/presentations/2013-10-05-dns-protocol.pdf
DNS OARC, October 2013

## Slide 15: TCP may not help here
If the fragmented response is lost (firewalls having issues with trailing fragments, PMTU signal loss, or network switches discarding IPv6 packets with Extension Headers) then the client gets no response at all, which is a signal of server failure
A non-responsive server may prompt a client to repeat the UDP query, which won’t help in this case.
This repeated unresponsive behaviour is not necessarily an invitation to re-query using TCP unless the client persists and re-issues the query with a small (or no) EDNS(0) UDP Buffer size option

## Slide 16: How can we measure this scenario of large DNS responses, DNS resolvers and IPv6?

## Slide 17: Our measurement approach
We use the Ad platform to enroll endpoints to attempt to resolve a set of DNS names:
  Each endpoint is provided with a unique name string (to eliminate the effects of DNS caching)
  The DNS name is served from our authoritative servers
  Each DNS name contains a name creation time component (so that we can disambiguate subsequent replay from original queries)

## Slide 18: Experiment Parameters
Three DNS response sizes:
  Small – 169 octet IPv6 packet response
  Medium – 1,428 octet IPv6 packet response
  Large – 1,886 octet IPv6 payload
Operate the experiment’s servers in V6 only, using a 1,280 octet MTU on the DNS server
If the client’s DNS resolvers can successfully resolve the DNS name they they will fetch the named web object, so the measurement here is one of the failure rate to access the web object

## Slide 19: Dual Stack Resolvers
Not every resolver can perform a DNS query using IPv6
48% of the 65M experiments could not use the DNS over IPv6 to query for the name server record

## Slide 20: IPv6 DNS Resolution Results
48% of the 65M experiments could not use the DNS over IPv6 to query for the name server record
Of those that did, we observed the following Loss Rates in fetching the web object:
SMALL: 7%
MEDIUM: 42%
LARGE: 42%

## Slide 21: Who, where why?
Are there regional differences?
We use three different servers, and divide (roughly) clients into three geo areas: Americas, Europe & Africa, Asia & Oceania
LOSS RATE Americas Europe Asia
SMALL 4% 5% 13%
MEDIUM 23% 49% 52%
LARGE 24% 50% 52%

## Slide 22: V6, the DNS and Large Responses
A V6 only-Authoritative DNS Server serving UDP fragmented DNS responses appears to have significant problems in delivering this UDP fragmented response to recursive resolvers in the Internet
However the 7% loss rate for the unfragmented DNS response points to a high noise rate in the data collected using this experimental technique

## Slide 23: Can we identify these resolvers?
This is a challenging problem:
  An Extension Header packet drop is a silent drop
    no ICMP6 notification back to the sender
  The recursive resolver will receive no answer to its query, and will be unable to answer back to the stub resolver. However it may elect to re-query the authoritative server before giving up
  A stub DNS resolver client will time out on the query to a recursive resolver, and may re-query to other recursive resolvers before giving up

## Slide 24: Second Experiment
We created a ”glueless” delegation in the DNS
  The response to the query to the ‘parent’ lists the name servers of the ‘child’, but deliberately withholds the IP address of these name servers in the response. i.e. the response is missing the ‘glue’ records for the name servers
    We do this on the fly to ensure that each query name is unique, to ensure that there is no unintended side effect from DNS caching
  We then inflated the response of the name server record by adding pad records to the response
  The idea is that the name will only be resolved if the resolver is capable of receiving a large response when trying to chase down the name server addresses

## Slide 25: “Glueless” Delegation
“Parent” name server
“Sibling” name server
“Child” name server
The “child” name server will only be queried if the resolver could receive the response from the sibling name server
Reply with the DNS names of the name servers, but not their IP addresses
Secondary objective: resolve these
name server names to their IP addresses
Resume the original name resolution task

## Slide 26: “Glueless” Delegation
“Parent” name server
“Sibling” name server
“Child” name server
The “child” name server will only be queried if the resolver could receive the response from the sibling name server
Reply with the DNS names of the name servers, but not their IP addresses
Secondary objective: resolve these
name server names to their IP addresses
Resume the original name resolution task
We make this sibling response large, so that we can use the queries at the child to determine if the resolver can receive these large responses?

## Slide 27: Fail!
Many resolvers deliberately omit EDNS(0) options in their queries to chase down name server addresses
  As these records are not part of a subsequent DNSSEC validation pass then any DNSSEC records, such as RRSIG records are not needed, and most responses will be under 512 bytes in any case
  And those that are not under 512 will be truncated, allowing the resolver to re-ask the query using TCP
But we wanted to pass the resolver a large fragmented UDP response to see if received it
If we can’t do “large fragmented” can we just do “fragmented”?

## Slide 28: “Glueless” Delegation and Gratuitous IPv6 Fragmentation
“Parent” name server
“Sibling” name server
“Child” name server
The “child” name server will only be queried if the resolver could receive the response from the sibling name server
Reply with the DNS names of the name servers, but not their IP addresses
Secondary objective: resolve these
name server names to their IP addresses
Resume the original name resolution task
Use a heavily modified DNS server that fragments all DNS responses, irrespective of their size!

## Slide 29: V6, the DNS and Fragmented UDP Responses
We used the Ad platform to enroll endpoints to attempt to resolve a DNS name that included a IPv6 fragmented UDP response when attempting to resolve the name server’s name
Total number of tests: 10,851,323
Failure Rate in receiving a large response: 4,064,356
IPv6 Fragmentation Failure Rate: 38%

## Slide 30: Where?
Regionally there are slightly different outcomes:
  Asia Pacific: 31% Failure
  Americas: 37% Failure
  Eurasia & Africa: 47% Failure

## Slide 31: Which Resolvers?
10,115 IPv6 seen resolvers
3,592 resolvers were consistently unable to resolve the target name (likely due to failure to receive the fragmented response)
Which is too large a list to display here
But we can show the top 20…

## Slide 32: Individual IPv6 Resolvers in Which Networks?
All these resolvers appears to be unable to receive fragmented UDP
DNS responses – This is the Top 20, as measured by the query count
per resolver address

## Slide 33: Resolver ‘Farms’ in Which Networks?
This is the total per origin AS of those resolvers that appear to be unable to receive fragmented UDP DNS responses. This is the Top 20, as measured by the query count per origin AS

## Slide 34: What’s the Problem?
Extension Headers require that any transport protocol-sensitive functions in switches need to unravel the packet header’s extension header chain
  This takes a variable number of cycles for the device
  This is an anathema to a switch
  And passing through extension headers that the switch does not understand or not prepared to check is a security risk
  Easier to drop all packets with extension headers!
  See RFC 7872

## Slide 35: What can we do about it?
A. Get all the deployed routers and switches to accept packets with IPv6 Fragmentation Headers

## Slide 36: What can we do about it?
B. Alter the way IPv6 describes packet fragmentation

## Slide 37: What can we do about it?
C. Move the DNS off UDP

## Slide 38: Which Means…
We can try and ensure that there will always be enough IPv4 around to keep the DNS running over UDP long after all other traces of IPv4 in the Internet have been extinguished
Or we could try and constrain the bloat pressure in the DNS to keep responses from pushing into UDP fragmentation
Or think about moving to a different approach to the carriage protocol for the DNS in an IPv6 environment

## Slide 39: Seriously
If we are going to take a future of an IPv6-only Internet seriously we are going to have to take the concept of a DNS over IPv6 equally seriously
Which means that we need to figure out how to change the appalling drop rate for fragmented UDP responses for DNS over IPv6 in today’s network

## Slide 40: Some current ideas
Change the protocol behaviour?
  Shift Additional Records into additional explicit UDP query/response transactions rather than bloating the original DNS response
  ATR: Add a truncated response to trail a fragmented response
Change the transport:
  DNS over TCP by default?
  DNS over TLS over TCP by default?
  DNS over QUIC?
  Devise some new DNS framing protocol that uses multiple packets?

## Slide 41: Acknowledgements and Thanks
Google has supported our efforts to conduct this measurement since its inception, and continues to support us.
ICANN provide support for this measurement activity, particularly relating to our measurement of DNS and DNSSEC capabilities
ISC for a conveniently located server at PAIX
Fernando Gont’s IPv6 toolbox provided valuable hints on the raw IPv6 packet handling routines we developed to perform IPv6 fragmentation handling tests
And thanks to Ray Bellis for development of the original dynamic DNS server code

## Slide 42
Thanks!