## Slide 1: Measuring the End User
Geoff Huston
APNIC Labs

## Slide 2: How to measure “the Internet”
What do we mean when we say
  “we’re measuring the Internet?”

## Slide 3: Measurement Self-Selection
When we first looked at measuring in the Internet, it was all about the network, and the distinction between network management and network measurement was not very clear
We ended up measuring what’s easy to measure and often missed measuring what’s useful to understand

## Slide 4
User experience
  Responsiveness
  Sustained Throughput
  Application performance quality
  Consistency
  Availability
Network Behaviour
  Routing Stability
  Path characteristics
Element Behaviour
  Subnet characteristics
  Switch element behaviour
  Switch resource consumption
Network availability
  Element availability
  Transmission path availability
  Transmission element BER
  Network path availability
Path characteristics
  Latency
  Jitter characteristics
  Loss characteristics
Protocol behaviour
  Transport protocol behaviour
  IPv6 penetration levels
  Failover behaviour
  Connection failures
And so on...

## Slide 5: What are you trying to measure?
User experience
  Responsiveness
  Sustained Throughput
  Application performance quality
  Consistency
  Availability
Network Behaviour
  Routing Stability
  Path characteristics
Element Behaviour
  Subnet characteristics
  Switch element behaviour
  Switch resource consumption
Network availability
  Element availability
  Transmission path availability
  Transmission element BER
  Network path availability
Path characteristics
  Latency
  Jitter characteristics
  Loss characteristics
Protocol behaviour
  Transport protocol behaviour
  IPv6 penetration levels
  Failover behaviour
  Connection failures
And so on...

## Slide 6: Network Measurement Approaches
PING and related probe techniques
  Send an ICMP echo request to a target device and measure the time to respond
  Often used to interpret some indication of delay, loss and jitter
  BUT has little relationship to application performance, as the probe measurement is heavily impacted by the behaviour of the probe and the echo point
    i.e. beyond being a remote device availability beacon, its of little practical use

## Slide 7: Network Measurement Approaches
SNMP and device polling
  Per-element probe to poll various aspects of an element’s current status
  Of little practical value in determining end-to-end network performance, as there is a distinct gap between end-to-end path performance and periodic polling of network element state

## Slide 8: Network Measurement Approaches
Active Test Traffic
  Perform a particular network transaction in a periodic fashion and correlate application performance across invocations
  Often measures the performance limitations of the test gear and the target rather than the network
  Tests only a small number of network transit paths
  Provides only a weak correlation between measurement results and actual end-user experiences of application performance

## Slide 9: What, Where and Why?
Using a combination of active and passive measurement techniques there is a massive set of possible aspects of network behaviour that can be measured
Few network measurements have any real bearing on the performance characteristics of applications that include some form of network interaction
  i.e. there’s a difference between measuring any old thing and measuring something relevant and useful
If you are going to measure something…
  Know why you are measuring it
  Understand the limitations of the measurement technique
  Understand the limitations of any interpretation of the measurement
  Understand who is the consumer of the measurement

## Slide 10: IP Performance
The end-to-end architectural principle of IP:
  The network should not duplicate or mimic functionality that can or should be provided through end-to-end transport-level signalling
  Wired IP networks can be seen as lossy queue-controlled passive switching devices connected through fixed delay channels
  Wireless IP networks are worse!
IP parameters:
  Delay
  Delay stability
  Jitter
  Loss rate
  Loss burstiness
In general the smaller the numbers the better, but ...

## Slide 11: TCP Performance
TCP performance is the interaction of concurrent end-to-end transport sessions performing a role of mutually enforced resource sharing
  The network is not a mediator or controller of an application’s resource requirements
Its a lot like fluid dynamics:
  Each network transport flow behaves in a fair greedy fashion, consuming as much of the network’s resources as other concurrent network transport applications will permit

## Slide 12: Observations
Most networks are a collection of elephants and rats
  And the elephants are uncontrollable
  And the rats breed like crazy
If all the traffic is long-held TCP and buffers are “right”-sized then the traffic should drive a network to oscillate around the point of packet loss
If all the traffic is inelastic then congestion events can become catastrophic

## Slide 13: Approaches to Measurement...
Measure the network
  And claim that perfection is in the eye of the network management system
  And everything else is a user problem!
This approach has its weaknesses of course

## Slide 14: Maybe asking how to measure “network performance” is the wrong question
How well your car operates is an interaction between the functions and characteristics of the car, the behavior of other cars, and the characteristics of the road
How well an application operates across a network is also an interaction between the application and the local host and the interaction by its remote counterparts and their hosts as well as the interaction between the application’s transport drivers and other concurrent applications that occur within the network

## Slide 15: The Internet is all about users and use!

## Slide 16: Measuring the End User

## Slide 17: The Challenge:
How can we undertake meaningful public measurements that:
quantify aspects of users’ experiences
drawn from across the entire Internet
that don’t rely on access to private data?

## Slide 18: For example… IPv6
It would be good to know how we are going with the transition to IPv6
And it would be good everyone to know how everyone else is going with the transition to IPv6

## Slide 19: For example… IPv6
What can we measure?
  IPv6 in the DNS – AAAA records in the Alexa top N
  IPv6 in routing – IPv6 routing table
  IPv6 traffic exchanges – traffic graphs
What should we measure?
  How many connected devices on today’s Internet are capable of making IPv6 connections?

## Slide 20: Approaches to Measurement...
From the inside looking out
  Set up a measurement station
    Ping, traceroute and fetch routines
    Measure the absolute outcomes and the variance
  Its not really a user metric
    It’s not that bad
    But its not that useful either

## Slide 21: Approaches to Measurement...
From the outside looking in:
  Set up a measurement station
    Enrol end users to send traffic to it
    Measure the absolute outcomes and the variance
  Or instrument your web server
  Its not a bad metric
    But its a small sample set that is often nerd heavy
    And nerds are “special”

## Slide 22: Approaches to Measurement...
From the inside looking out
  RIPE Altas
    Many thousands of end points installed in end user networks
    Ping and traceroute to a small set of destinations
    And report back
    Analysing the data to produce relevant outcomes is a challenge

## Slide 23: Approaches to Measurement...
From the inside looking out
  The “Sam Knows” approach
    “be the user”
    Use a known common platform (Open WRT DSL modem)
    Use a common set of tests (short and large data transfer)
    Take over the user’s connection and perform the tests at regular intervals
    Report results
  Originally developed to test DSL claims in the UK
  Used by the FCC and ISPs in the US
  Underway in Singapore and in Europe

## Slide 24: Observations
IP performance measurement is not a well understood activity with mature tools and a coherent understanding of how to interpret various metrics that may be pulled out from hosts and networks
The complex interaction of applications, host systems, protocols, network switches and transmission systems is at best only weakly understood
  But there’s a lot of slideware out there claiming to provide The Answer!

## Slide 25: How to measure millions of end devices for their IPv6 capability?

## Slide 26: How to measure millions of end devices for their IPv6 capability?
a) Be

## Slide 27: How to measure millions of end devices for their IPv6 capability?
OR
Have your measurement code run on a million end devices

## Slide 28: Approaches to Measurement
A case study: APNIC’s approach
we wanted to measure IPv6 deployment as seen by end users
We wanted to say something about ALL users
So we were looking at a way to sample end users in a random but statistically significant fashion
We stumbled across the advertising networks...

## Slide 29: …buy the user!

## Slide 30: Ads are ubiquitous

## Slide 31: Ads are ubiquitous

## Slide 34: The Ad Measurement Technique
End user
Ad Server
Authoritative Name Server
Web Server

## Slide 35: The Ad Measurement Technique
End user
Ad Server
Authoritative Name Server
Web Server
1. Ad Impression

## Slide 36: The Ad Measurement Technique
End user
Ad Server
Authoritative Name Server
Web Server
DNS Resolvers
2. DNS resolution

## Slide 37: The Ad Measurement Technique
End user
Ad Server
Authoritative Name Server
Web Server
3. Web Fetch

## Slide 38: The Ad Measurement Technique
End user
Ad Server
Authoritative Name Server
Web Server
4. Result Web Fetch

## Slide 39: What can be scripted
Not much:
  http.FetchImg()
    i.e. attempt to retrieve a URL
But that’s enough!
  It’s EXACTLY what users do!
  A URL consists of a DNS question and an HTML question
  What if we point both the DNS and the HTML to servers we run?
  As long as each Ad execution uses unique names we can push the user query back to our servers

## Slide 40: Tests
Think of a URL name as a microcoded instruction set directed to programmable DNS and HTTP servers …
http://06s-u69c5b052-c13-s1579128735-icb0a3c4c-0.ap.dotnxdomain.net/v61x1.png
IPv6 access only
Valid DNSSEC signature available
User is located in Country 13 (Australia)
Time is 16 January 2020 9:52am
User’s IPv4 address is 203.10.60.76
Valid DNS

## Slide 41: Ad Placement
At low CPM, the advertising network needs to present unique, new eyeballs to harvest impressions and take your money.
  Therefore, a ‘good’ advertising network provides fresh crop of unique clients per day

## Slide 42: Unique IPS?
Collect list of unique IP addresses seen
  Per day
  Since inception
Plot to see behaviours of system
  Do we see ‘same eyeballs’ all the time?

## Slide 43: Lots of Unique IP’S
Unique IPs via Ads
Unique IPs via Web Sites

## Slide 44: Ad Presentation Volumes

## Slide 45: Ad Presentations: Countries

## Slide 46: Bias Compensation
The ad presentation is NOT uniform across the Internet’s user population
  The ad machinery ‘over-presents’ in some countries:

## Slide 47: Bias Compensation
The ad presentation is NOT uniform across the Internet’s user population
  The ad machinery ‘under-presents’ in some countries:

## Slide 48: Bias Compensation
Use ITU data on Internet users per country as the reference set, and weight the ad results to compensate for ad placement bias

## Slide 49: Dealing with the data
Unified web logs, dns query logs, packet capture
Map individual DNS and HTML transactions using a common experiment identifier
For example:
  DNSSEC validation implies:
    DNS queries include EDNS(0) DNSSEC OK flag set
    See DNS queries for DNSSEC signature records (DNSKEY / DS)
    User fetches URL corresponding to a validly signed DNS name
    User does not fetch URL corresponding to a in validly signed DNS name

## Slide 50: What are we measuring?
IPv6 adoption
IPv6 performance
IPv6 Extension header fragility
IPv4 and IPv4 Packet fragmentation resilience
DNS resolver centrality
DNS performance
DNSSEC validation
DNS over TCP
DNS NSEC caching

## Slide 51: What are we seeing?

## Slide 52: IPv6 Adoption by Country

## Slide 53: IPv6 Performance

## Slide 54: DNSSEC validation by Country

## Slide 55: Users per Network

## Slide 56: DNS Resolver Centrality

## Slide 57: Zombies
Remember the use of the current time in the URL?
We can distinguish between “current” and “old” DNS and HTML queries

## Slide 58: But…
It’s not a general purpose compute platform, so it can’t do many things
  Ping, traceroute, etc
  Send data to any destination
  Pull data from any destination
  Use different protocols
This is a “many-to-one” styled setup where the server instrumentation provides insight on the inferred behaviour of the edges

## Slide 59: Measurement Ethics
There is no user consent
And cookies (even “don’t measurement me!” cookies) are progressively being frowned upon
Don’t generate large data volumes
Don’t publish PII
Don’t use ‘compromising’ URL names

## Slide 60: In Summary…
Measuring what happens at the user level by measuring some artifact or behaviour in the infrastructure and inferring some form of user behaviour is always going to be a guess of some form
If you really want to measure user behaviour then its useful to trigger the user to behave in the way you want to study or measure
The technique of embedding simple test code behind ads is one way of achieving this objective
  for certain kinds of behaviours relating to the DNS and to URL fetching

## Slide 61
Thank You
Discussion?
labs