## Slide 1: An Update on IPv6 Fragmentation
Geoff Huston and Joao Damas
APNIC Labs

## Slide 2
Version
IHL
Total Length
Flags
Identification
Fragment Offset
Time To Live
Source Address
Destination Address
Options
Padding
Protocol
Header Checksum
Type of Service
Version
Class
Flow
Payload Length
Hop Limit
Source Address
Destination Address
Next Header
IPv4 Header
IPv6 Header
IPv6: Packet Header Changes
These three fields in the IPv4 header were pushed into the Extension Header chain, and do not appear in every IPv6 packet
This is a new field

## Slide 3: IPv6: Packet Header Changes
Type of Service changed to Traffic Class
  (yet to find a useful agreed role, even ECN!)
A Flow Label added
  (but yet to find a useful role!)
Header Checksum becomes a media layer function
Options, Protocol fields replaced by chained Extension Headers
Packet ID and Fragmentation Controls become an Extension Header

## Slide 4: IPv6: Packet Header Changes
Type of Service changed to Traffic Class
  (yet to find a useful agreed role, even ECN!)
A Flow Label added
  (but yet to find a useful role!)
Header Checksum becomes a media layer function
Options, Protocol fields replaced by chained Extension Headers
Packet ID and Fragmentation Controls become an Extension Header
The substantive change with IPv6 is the handling of Fragmentation and the use of Extension Headers

## Slide 5: Initial Tests: 2014 (RFC 7872)
August 2014 and June 2015
Sent fragmented IPv6 packets towards “well known” IPv6 servers (Alexa 1M and World IPv6 Launch
Drop Rate:
This is bad!
Really bad!

## Slide 6: Why so high?
Some possible reasons for the high drop rate:
Packet Fragments are often dropped by firewalls
IPv6 Path MTU measures rely on ICMPv6 (as there is no ability for the router to fragment on the fly), and ICMP exposes security vulnerabilities
Extension Header chains may either not be supported in router, or may only supported in the processor path (slow path)

## Slide 7
IPv6 Fragmentation Extension Header Handling
The extension header sits between the IPv6 packet header and the upper level protocol header for the leading fragged packet, and sits between the header and the trailing payload frags for the trailing packets
Practically, this means that transport-protocol aware packet processors/switches need to decode the extension header chain, if its present, which can consume additional cycles to process/switch a packet – and the additional time is not predictable. For trailing frags there is no transport header!
Or the transport-protocol aware unit can simply discard all IPv6 packets that contain extension headers!
IPv6 header
Payload
TCP/UDP xtn header
Fragmentation extn header

## Slide 8
Are the effects of middleware symmetric?
The RFC7872 experiments sent altered IPv6 packets towards well-known servers and observed whether the server received and reconstructed the altered packet by seeing whether the server responded (or not)
Sending large fragmented queries towards servers is not all that common – the reverse situation of receiving big responses is more common
What happens if we try to reproduce this experiment by looking at what happens when we send various forms of altered IPv6 packets back from servers – what’s the drop rate of this reverse case for packets from servers to end-clients?

## Slide 9
IPv6 Fragmentation Extension Header Handling
We used an ad-based measurement system, using a custom packet fragmentation wrangler as a front end to a DNS and Web server to test IPv6 fragmentation behaviour
Client
DNS Resolver
IPv6 DNS Server
IPv6 Web Server
IPv6 ‘Fragmenter’
DNS Goo
Fragmented packets

## Slide 10: APNIC Test – August 2017
Use APNIC IPv6 measurement platform to test the drop rate of IPv6 packets flowing in the opposite direction (server to client)
This is an improvement over
the RFC7872 measurement,
which reported a 28% drop rate
client to server

## Slide 11: APNIC Test - 2021
Re-work of the 2017 measurement experiment
  Same server-to-client TCP session fragmentation mechanism
  Uses a dedicated middlebox to fragment outgoing packets to improve packet handling capacity of the experiment
  drop is detected by a hung TCP session that fails to ACK the sequence number in the fragmented packet
  This time we randomly vary the initial fragmented packet size between 1,200 and 1,416 bytes
  Performed as an ongoing measurement

## Slide 12: IPv6 Packet Mangler Design
Easier said than done when we are limited to user-space code on standard cloud processing platforms
We needed a promiscuous capture mechanism that works in user space. We used the libpcap libraries to perform packet capture, and used IP packet filters to stop the kernel’s persistent desire to send RST packets
The problem is that the pcap libraries have no buffers so were are dropping packets under load. We resorted to using multiple processes and shared memory ring buffers to improve throughput
We also split the back end server and the packet mangling function to separate units, so we also implemented an IPv6 NAT function in the packet mangler again as a shared memory structure
Input
capture
Input
capture
Shared
Ring Buffer
Shared
Ring Buffer
Shared
NAT table
IPv6
NAT
IPv6
NAT +
Packet Fragmenter
External
Client
Server
Packet Mangler

## Slide 13: 2021 Fragmentation Drop Rate
This is a significant improvement over 2017 data
Since 2017 there are 10x the number of IPv6 users and the fragmentation drop rate has come down by 2/3 – we appear to be getting better at handling IPv6 fragments in the longer term!

## Slide 14: 2021 Fragmentation Drop Rate
More recent IPv6 deployments appear to be better at frag handling than more mature ones

## Slide 15: Drop Rate by Size
This is unexpected. Why does the drop rate increase so markedly when the fragmented packet size passes over the threshold of 1,360 octets?

## Slide 16: Drop Size Profile by Region
Americas
Europe
Asia

## Slide 17: Why?
Drop patterns vary across service providers, so there are probably contributary factors from network equipment and configurations
4% Drop!
95% Drop!
This was us!

## Slide 18: Why?
Other potential factors that could contribute:
Local security policies in user-facing edge devices
IPv6 EH may trigger “slow path” processing in network equipment that could lead to higher drop rates
IPv6 Path MTU woes!
TCP MSS settings interfere with the measurement

## Slide 19: Frag Drop or EH Drop?
We added a further test to try and see the difference between Fragmentation and Extension Headers
  We used an ”atomic” fragment, which is a IPv6 packet with a Fragmentation Header where the fragment offset is 0 and the M (more) bit is also 0

## Slide 20: 2021 Fragmentation Drop Rate
Atomic Fragment drop rate is 6%

## Slide 21: Frags vs Atomic Frags
Most of the time the Atomic Frag drop rate is ~3x lower than the Fragmented packet drop rate
Except when it’s not!

## Slide 22: Frag Drop or EH Drop?
The Atomic Frag data isn’t really as informative as we would’ve liked
We thought that all hosts would accept incoming packets with an Atomic Frag header
  After all the Atomic Frag header is a no-op for the packet!
So if there are Atomic Frag packet drops it should be a network effect
  The Atomic Frag drop rate should always be less than the fragmented packet drop rate
But this is not always the case in our data
So we looked for other Extension Headers to test

## Slide 23: EH DST Drop?
What’s another innocuous Extension Header we can use?
There is the PADN Destination Option
  In this way can can compare the network treatment of extension headers to the treatment of fragmentation headers
Let’s use it!
  Because padding does not relying on any particular functionality in the host, so hosts should accept it
In theory Destination Options should be handled by the network as a neutral option, as the option signalling is about the destination host, not the network elements that switch the packet in transit

## Slide 24: Destination Option Drop Rate
January 2022: 94.5% drop rate
Wow! That’s awesomely bad!
It seems that most hosts are dropping incoming packets with unexpected destination options, whether they contain directives of just padding or other directives, but we need to test this against various commonly used IPv6 protocol stacks to test this a little more

## Slide 25: EH HBH Drop?
What’s another innocuous Extension Header we can use?
There is the PADN Hop-by-Hop Option
  In this way can can compare the network treatment of extension headers to the treatment of fragmentation headers
Let’s try this
  Because padding does not relying on any particular functionality in the host, so hosts should accept it
Again, this is a simple padding option so no special processing is being requested from the network’s switches

## Slide 26: Hop-by-Hop Option Drop Rate
February 2022: 99.5% drop rate
Wow! That’s awesomely even badder!
It seems that most hosts and routers are dropping incoming packets with destination and hop-by-hop options, but we need to test this some more

## Slide 27: Summary
The network is slowly improving it’s handling of fragmented IPv6 packets
  In 5 years its gone from unusably bad to tolerably poor
  Recent IPv6 deployments appear to show more robust general handling of IPv6 packets
Destination Extension Headers and Hop-by-Hop Extension Headers are not usefully supported on public Internet infrastructure

## Slide 28: Lessons Learned on Fragmentation
Don’t Fragment outgoing packets
Don’t rely on PMTUD
More generally, don’t rely on Extension Headers nor on ICMP6 integrity
Pick your TCP MSS setting carefully:
  1280 is a robust local MTU size – but possibly too conservative
  1350 is survivable as a MTU size – the Goldilocks choice
  1400 is risky – but survivable in most cases
  1500 is a poor choice – this leads to visible failure cases

## Slide 29: Lessons Learned on HBH and Dst EHs
Don’t

## Slide 30: Daily Report
https://stats.labs.apnic.net/v6frag

## Slide 31: That’s it!