## Slide 1: On GEOs, LEOs and Starlink
Geoff Huston
APNIC

## Slide 2
screenshot from starwatch app
Screenshot: https://asia.nikkei.com/Business/Telecommunication/Elon-Musk-s-Starlink-launches-satellite-internet-service-in-Japan
Screenshot - https://www.theverge.com/2022/8/25/23320722/spacex-starlink-t-mobile-satellite-internet-mobile-messaging
LEOs in the News

## Slide 3: Newtonian Physics
If you fire a projectile with a speed greater than 11.2Km/sec it will not fall back to earth, and instead head away from earth never to return
On the other hand, if you incline the aiming trajectory and fire it at a critical speed it will settle into an orbit around the earth
The higher the altitude, the lower the orbital speed required to maintain orbit

## Slide 4: Solar Radiation Physics
The rotating iron core of the Earth produces a strong magnetic field
This magnetic deflects solar radiation – the Van Allen Belt
Sheltering below the Van Allen Belt protects the spacecraft from the worst effects of solar radiation, allowing advanced electronics to be used in the spacecraft

## Slide 5
https://commons.wikimedia.org/wiki/File:Orbitalaltitudes.jpg GNU Free Documentation License
Leos
Geos

## Slide 6: Geostationary Earth Orbit
At an altitude of 35,786km a satellite will orbit the earth with the same period as the earth’s rotation – from the earth it will appear to be stationary in the sky
https://secure.boeingimages.com/archive/Commercial-Communications-Satellites-Orbit-2F3XC5KQCM9.html
https://commons.wikimedia.org/wiki/File:Communications_satellite_with_TEMPO_spacecraft_model.png – public domain

## Slide 7
Low Earth Orbit
https://commons.wikimedia.org/wiki/File:Orbitalaltitudes.jpg GNU Free Documentation License

## Slide 8: Low Earth Orbit
LEO satellites are stations between 160km and 2,000km in altitude.
High enough to stop it slowing down by “grazing” the denser parts of the earth’s ionosphere
Not so high that it loses the radiation protection afforded by the Inner Van Allen belt.
At a height of 550km, the minimum signal propagation delay to reach the satellite and back is 3.7ms.
screenshot from starwatch app
Image - spacex

## Slide 9: Geo Coverage
Source: Viasat
It needs just 3 GEO satellites to provide global continuous coverage everywhere (except polar)

## Slide 10: LEO coverage
It needs a minimum of some 500 LEO satellites to provide global continuous coverage everywhere (at 550km altitude)
Depending on the quality of coverage you are after, you may need some thousands of LEO spacecraft!

## Slide 11: So LEOs are “interesting”!
They are very close to the Earth – which means:
  They don’t need specialised high-power equipment to send and receive signals
    Even hand-held mobile devices can send and receive signals with a LEO!
  They can achieve very high signal speeds
    It’s a highly focussed signal beam
But you need a large number of them to provide a continuous service
  Each satellite spans footprint of no more than ~900Km radius, or 2M K2
  At a minimum you’ll need 500 satellites to provide continuous coverage
  But if you want high quality coverage you are going to need 6x-20x that number (or more)
The extremely host cost of launching a large constellation of LEO spacecraft has been the major problem with LEO service
  Which is why Motorola’s Iridium service went bankrupt soon after launch

## Slide 12: What’s changed recently?
SpaceX’s reusable rocket technology has slashed the cost of lifting spacecraft into low earth orbit
SpaceX
https://ourworldindata.org/grapher/cost-space-launches-low-earth-orbit
Cost/Kg (log scale)
Time

## Slide 13
Current and Planned satellite constellations

## Slide 14: Low altitude: smaller footprint

## Slide 15: Tracking a LEO satellite
550km
27,000 km/h
Satellite
horizon to horizon: ~5 minutes

## Slide 16: Earth Dishes for LEOs
Just overkill!
(in every possible way!)

## Slide 17: Earth Dishes for LEOs
Still too big
And it needs to be steered

## Slide 18: Earth Dishes for LEOs
Phased array antennae
An array of smaller antenna with software-controlled phase alignment means that the dish can steer its focal angle in two dimensions with minimal lag
This is ideal for LEO systems which use low power but high traversal speed
Small, light, cheap, self-aligning!

## Slide 19: Self Installed!

## Slide 20: Gen1 vs Gen2
GEN 1 – “mirror in the sky”
client
Earth station
This approach is limited by the number and location of earth stations. Earth stations need to be located within 900km of the clients
This approach cannot span large ocean spaces

## Slide 21: Gen1 vs Gen2
GEN 2 – Inter-Satellite laser Links
client
Earth station
This approach equips the satellites with laser transmitters and receivers
Signals can be relayed to adjacent satellites in the ”train” to hop across spaces where there is no coverage by earth stations

## Slide 22: ISL in action
The introduction of ISL has allowed Starlink to extend its coverage area to the entirety of the Australian continent, and it manages this by relaying the signal between spacecraft to one that is within range of an earth station

## Slide 23: How well does all this work?
Let’s measure it!
We use three services between the same endpoints:
  Terrestrial fibre connection (control)
  GEO satellite service
  Starlink service
We also use three TCP flow control algorithms to compare their performance

## Slide 24: TCP Flow Control Algorithms
“Ideal” Flow behaviour for each protocol

## Slide 25: Terrestrial Fibre
Australian NBN FTTP service with a 275/25 Mbps access rate
Server and client are some 1,000km apart
Ping test:
IPv4 average 20.5ms
IPv6 average 21.5ms

## Slide 26: Fibre – 2 Stream Reno
Data Rate (MBPS)

## Slide 27: Fibre – 2 Stream Cubic

## Slide 28: Fibre – 2 Stream BBR

## Slide 29: Protocol Performance over Fibre
All three congestion control algorithms are “well behaved” in this simple test
Reno and BBR equilibrate to a 50/50 share when 2 sessions are active, while Cubic stabilises at a 60/40 split
BBR operates with very small queue pressure, and stabilises at wire speed very quickly

## Slide 30: GEO Service – (45Mbps service)
Ping profile

## Slide 31: GEO – 2 Stream Reno

## Slide 32: GEO – 2 Stream Cubic

## Slide 33: GEO – 2 Stream BBR

## Slide 34: Protocol Performance over a GEO circuit
While the ping times are relatively stable, the extended RTT time pushes the congestion protocol into areas of instability – this is likely due to the presence of deep queues in this product, in conjunction with the high delay of the path
Both Reno and Cubic drop into instability after some 60 seconds. It is unclear whether this is protocol breakdown, or the impact of cross traffic on the tested flows within the GEO system
BBR operates remarkably efficiently across this system, driving the link to the delivered capacity without the build up of a standing queue - clearly BBR out-performs Reno and Cubic in this context

## Slide 35: Starlink service
https://satellitemap.space/

## Slide 36: Starlink service
3,840 in-service operational spacecraft, operating at an altitude of 550km
https://satellitemap.space/

## Slide 37: Starlink service
3,840 operational spacecraft, operating at an altitude of 550km
One-way signal propagation time to reach the spacecraft varies between 1.8ms and 3.6ms (equivalent RTT of 7.3ms to 14.6ms)
But that’s not what we see:
2000 packets transmitted, 1991 received, 0.45% packet loss, time 2009903ms rtt min/avg/max/mdev = 37.284/60.560/214.301/13.549 ms

## Slide 38: Starlink RTT Ping Times
We are seeing:
12ms terrestrial component,
7ms/14ms propagation component,
30ms for codec/fec/switching?

## Slide 39: Starlink – 2 Stream Reno
Relatively unimpressive performance.
There appears to be imposed packet loss events that hampers Reno inflating the sending rate

## Slide 40: Starlink – 2 Stream Cubic
Also unimpressive performance.
Cubic appears to be more stable than Reno, but still fails to open up its sending rate over time, so the higher stability is achieved at a cost of lower overall throughput

## Slide 41: Starlink – 2 Stream BBR
BBR seems to be better positioned to extract performance from a variable platform in loss and jitter terms- it is able to operate 3 – 5 times the speed of Cubic or Reno between the same endpoints
The packet loss rate is higher than expected, and this may be an outcome of the combination of using phase array antennae that are tracking satellites that are moving through the sky at a relative speed of 1 degree of elevation every 15 seconds, together with the need to perform satellite handover at regular intervals.

## Slide 42: Performance
Speedtest-measuremed capacity
1 second ping
Micro-drops

## Slide 43: Protocol Considerations
Starlink services have two issues:
  Very high jitter rates
  High levels of micro-loss
Loss-based flow control algorithms will over-react and pull back the sending rate
  Short transactions work well
  Paced connections (voice, zoom) tend to work well most of the time
  Bulk data transfer not so mucj
You need to move to less sensitive flow control algorithms, such as BBR to get good performance out of these services

## Slide 44: Measuring QUIC Performance
In this test (between the same endpoints) over a Starlink circuit, TCP CUBIC underperforms badly, while TCP BBR and QUIC both perform reasonably well

## Slide 45: More measurements needed …
Is iperf3 on Linux the right measurement tool?
Can we bypass the Linux kernel baggage and measure the ‘raw’ TCP protocol performance?
Would using QUIC provide a different view of protocol performance?
How do LEO services compare to 5G?
Speed vs stability?
  Should a LEO service expose the underlying jitter and loss to the application, or should it integrate smoothing, and even basic retransmission into the service at the cost of a higher delay overhead?

## Slide 46: What about Starlink Gen2?
These satellites are larger, heavier and operate at a higher power level
More bandwidth available, and high achievable data speeds
Multiple orbital plans at a collection of discrete altitudes
Incorporates 5G cellular services
Will use inter-satellite laser connectors to support packet routing across satellites – details sparse so far, and it’s not clear how flexible this will be in terms of routing in the mesh

## Slide 47: Does it scale?
Fibre – well yes, just bury more cable!
GEO – no, not really
  Geostationary spacecraft are normally separated by 2 – 3 degrees or arc, so there are some 120 – 180 viable slots. The radio frequencies are also limited to the C, Ku and Ka bands. The on-craft transponders are not steerable so the capacity is provided to a pre-designed footprint
LEO – unclear, but probably not
  LEO constellations use low altitude eccentric orbits so the number of space craft in a constellation is determined by the inter-craft distance, horizontally and vertically.
  Starlink plan for 12,000 craft, Kuiper (Amazon) place for 3,200, Telesat 188, ITU-R filings indicate China is planning a constellation with 13,000 craft
  There is an issue with space junk at LEO orbits. Any collision will generate more junk, and the risk of a runaway effect is high if the altitude slots are densely packed

## Slide 48: Questions?

## Slide 49: Questions?