## Slide 1: IPv6
Geoff Huston AM
Chief Scientist, APNIC

## Slide 2: What’s the problem? Up and to the right, yes?
IPv6 Adoption Rates
2015
2017
2019
2021
2023

## Slide 3: Oops!
IPv6 Adoption Rates
2015
2017
2019
2021
2023
30%
20%
10%
What’s the problem? Up and to the right, yes?

## Slide 4: It’s been around a decade…
Since the RIRs handed out their last substantial IPv4 address blocks
We’ve been in a state of IPv4 “address exhaustion” for more than a decade
And yet the global uptake rate of IPv6 is a little over one third of the Internet’s user base
This is completely unexpected!

## Slide 5: Projecting this Forward
2045

## Slide 6: Projecting this Forward
Another 20 years of transition?
Seriously??
2045

## Slide 7: What’s gone wrong here?

## Slide 8: Let’s head to the Time Machine
And dial it back by about 35 years!
https://creativecommons.org/licenses/by-nc-sa/2.0/
https://www.flickr.com/photos/tjjohn12/24398810050

## Slide 9: 1990 – Panic at the IETF!
The Internet was only just gathering momentum we were told that the address plan had just a few years to run before the Class B address pool would be fully depleted

## Slide 10: 1990 – Panic at the IETF!
The Internet was only just gathering momentum we were told that the address plan had just a few years to run before the Class B address pool would be fully depleted
Short term hack – remove the Class A/B/C structure from IP addresses (and routing)
Longer term solution – develop a new network design that encompassed a far larger scale of use…

## Slide 11: IPv6!

## Slide 12: IPv6!
Minimal changes to IP:
  Expand the address fields four-fold to 128 bits
    64-bit network prefix, 64-bit interface identifier
  Remove packet fragmentation-on-the-fly
  Replace ARP with Multicast

## Slide 13: But
But IPv6 was not backward compatible with IPv4 on the wire
The plan was that we needed to run some form of a “dual stack” transition process
  Network-level proxies/translators were deemed to be too insecure
Which meant that we needed to equip hosts and networks with two protocol stacks
But the network was too big to ”just do it” so we needed to devise a “transition plan” that allowed for piecemeal adoption

## Slide 14: Dual Stack Assumptions
That we could drive the entire transition to IPv6 while there were still ample IPv4 addresses to sustain the entire network and its growth
Transition would be driven by individual local decisions to deploy dual stack support
The entire transition would complete before the IPv4 unallocated pool was exhausted

## Slide 15: Dual Stack Transition to IPv6
Phase 1
“Initial” Dual Stack deployment:
  Dual stack networks with V6 / V4 connectivity
  Dual Stack hosts attempt V6 connection, and use V4 as a fallback

## Slide 16: Dual Stack Transition to IPv6
Phase 2
“Intermediate”
  Older V4 only networks are retro-fitted with dual stack V6 support

## Slide 17: Dual Stack Transition to IPv6
The Final Outcome
“Completion”
  V4 shutdown occurs in a number of networks
  Connectivity with the residual V4 islands via DNS ALG + NAT-Protocol Translation
  Outside the residual legacy deployments, the network is single protocol V6

## Slide 18: Problem solved!
We had a technology solution to address depletion
Because hosts preferred to use IPv6 when there was IPv6 available, the transition would operate automatically as networks enabled IPv6
So, we then shifted our collective attention elsewhere!
For the next decade or so
Until…

## Slide 19: 2009 - Inexorable Growth
IPv4 Address Allocations
1996 2000 2004 2008

## Slide 20: 2010 - Accelerating Growth
189.6 Million Addresses
248.8 Million Addresses
2009
2010

## Slide 21: Accelerating Growth
189.6 Million Addresses
248.8 Million Addresses
2009
2010

## Slide 22: We had this plan …
IPv6 Deployment
IPv4 Pool
Size
Size of the
Internet
IPv6 Transition using Dual Stack
Time

## Slide 23: But we had strayed off-plan!
IPv4 Allocated Addresses
IPv4 Advertised Addresses
IANA Free Pool
IANA Exhaustion February 2011
First RIR Exhaustion July 2011

## Slide 24: Where were we with IPv6 deployment?
http://www.google.com/intl/en/ipv6/statistics/

## Slide 25: Something wasn’t right!
We were meant to have completed the transition to IPv6 BEFORE we completely exhausted the supply channels of IPv4 addresses

## Slide 26: The 2011 IPv6 Transition Plan
IPv6 Deployment
2004
IPv6 Transition – Dual Stack
IPv4 Pool Size
Size of the Internet
2006
2008
2010
2012
Date
7 months!

## Slide 27: Was this Plan Feasible?
Deploy IPv6 across some 1.8 billion users, with more than a billion end hosts, and upgrade hundreds of millions of routers, firewalls, middleware units and CPEs, and audit billions of lines of configuration codes and filters, and audit hundreds of millions of ancillary support systems -
all within 200 days.

## Slide 28: The 2012 IPv6 Transition Plan
IPv6 Deployment
2004
IPv6 Transition – Dual Stack
IPv4 Pool Size
Size of the Internet
2006
2008
2010
2012
Date
?

## Slide 29: What next?
Despite the whinging from IETF purists over the compromise of a pristine end-to-end model there really was no other option:
The answer was NATs!

## Slide 30: NATs
This low friction response to IPv4 address depletion had been used for more than a decade in client/server network architectures
Clients initiate a service transaction and only need an external address/port binding for the duration of the transaction
Servers sit in central data centres and share platform IP addresses using name-based distinguishers

## Slide 31: Implications
IPv4 addresses continue to be in demand far beyond the date of exhaustion of the unallocated pool
  In the transition environment, all new and expanding network deployments will need IPv4 service access and addresses for as long as we are in this dual track transition
But the process is no longer directly controlled through today’s address allocation policies
  Address access for IPv4 addresses is mediated by market pricing
  And the large CDN actors appear to be dominating this space

## Slide 32: Making IPv4 Last Longer
For how long?
For what cumulative address demand?
For what level of fairness of access?
At what cost?
For whom?
To what end?
What if we actually achieve something different?
  How would the Law of Unintended Consequences apply here?
  Would this negate the entire “IPv6 is the solution” philosophy?

## Slide 33: Why is the Internet wedged on IPv6 transition?

## Slide 34: Not everyone is feeling the pressure to move to Dual Stack
2020
2022
2024
% of Users
https://stats.labs.apnic.net/ipv6/XQ

## Slide 35: Maybe this really is the IPv6 trajectory that we’re now locked into
2045!

## Slide 36: Why is the Internet wedged on IPv6 transition?
Because we no longer operate within a strict address-based network architecture
  Clients no longer use a permanent unique public IP address to communicate with servers
  Servers no longer use a permanent unique public IP address to communicate with clients
Address scarcity takes on a different dimension when you don’t need public addresses to uniquely number every host and service

## Slide 37: Because it wasn’t just an IPv4 to IPv6 transition
Follow the money…

## Slide 38: The “Classical” Internet
IP was a network protocol that provided services to attached devices
It was the role of Network Providers to allow clients to consume content and access services
  The costs of operating the network dominated the entire cost of the Internet
  In networking distance dominates all cost models
  In the Internet ecosystem the role of transit providers was paramount
    We used to spend all our time talking about peering and transit!
  ISPs were the brokers of rationing the scarce resource of distance capacity
media
network
transport
apps
$$$

## Slide 39: What’s driving change today?
From scarcity to abundance!
For many years, the demand for communications services outstripped available capacity
We used price as distribution function to moderate demand to match available capacity
But this is no longer the case – available capacity in the communications domain far outpaces demand

## Slide 40: Abundant Capacity
https://www.ncbi.nlm.nih.gov/
Fibre cables continue to deliver massive capacity increases within relatively constant unit cost of deployment
(That 2022 number is probably low – at the end of 2022 we can pull 2.2T per lambda with a 190Gbd signal rate, giving a fibre capacity of 105T)

## Slide 41: Abundant Compute Power
By Max Roser, Hannah Ritchie - https://ourworldindata.org/uploads/2020/11/Transistor-Count-over-time.png, CC BY 4.0, https://commons.wikimedia.org/w/index.php?curid=98219918

## Slide 42: Abundant Storage
http://aiimpacts.org/wp-content/uploads/2015/07/storage_memory_prices_large-_hblok.net_.png

## Slide 43: How can we use this abundance?
By changing the communications provisioning model from on demand to just in case
Instead of using the network to respond to users by delivering services on demand we’ve changed the service model to provision services close to the edge just in case the user requests the service
With this change we’ve been able to eliminate the factors of distance from the network and most network transactions occur over shorter network spans
What does a shorter network enable?

## Slide 44: Bigger
Increasing transmission capacity by using photonic amplifiers, wavelength multiplexing and phase/amplitude/polarisation modulation for fibre cables
Serving content and service transactions by distributing the load across many individual platforms through server and content aggregation
The rise of high-capacity mobile edge networks and mobile platforms add massive volumes to content delivery
To manage this massive load shift we’ve stopped pushing content and transactions across the network and instead we serve from the edge

## Slide 45: Faster
Reduce latency - stop pushing content and transactions across the network and instead serve from the edge
The rise of CDNs serve (almost) all Internet content and services from massively scaled distributed delivery systems.
The “Packet Miles” to deliver content to users has shrunk - that’s faster!
The development of high frequency cellular data systems (4G/5G) has resulted in a highly capable last mile access network with Gigabit capacity
Applications are being re-engineered to meet faster response criteria
Compressed interactions across shorter distances using higher capacity circuitry results in a much faster Internet

## Slide 46: Better
If “better” means “more trustworthy” and “more privacy” then we are making progress at last!
  Encryption is close to ubiquitous in the world of web services
  TLS 1.3 is moving to seal up the last open TLS porthole, the SNI field
  QUIC is sealing up the transport controls from the networks
  Oblivious DNS and Oblivious HTTP is moving to isolate knowledge of the querier from the name being queried
  The content, application, and platform sectors have all taken the privacy agenda up with enthusiasm, to the extent that whether networks are trustable or not doesn’t matter any more – all network infrastructure is uniformly treated as untrustable!

## Slide 47: Cheaper
We are living in a world of abundant comms and computing capacity
And working in an industry when there are significant economies of scale
And it’s being largely funded by capitalising a collective asset that is infeasible to capitalise individually – the advertisement market
The result is that a former luxury service accessible to just a few has been transformed into an affordable mass-market commodity service available to all

## Slide 48: And in all this, the money moved up the stack
media
network
transport
apps
Internal
Transport +
session security
$$$
media
network
transport
apps
$$$

## Slide 49: So, who needs to pay?
Networks need to make the investment to switch to a dual stack mode that includes IPv6
But neither the user base not the content world really care
  And they are certainly not going to pay a premium to the network operator for IPv6
And in the application service world IP addresses are not the critical resource
We’ve changed the “currency” of networks

## Slide 50: A Network of Names
Today’s public Internet is largely a service delivery network using CDNs to push content and service as close to the user as possible
The multiplexing of multiple services onto underlying service platforms is an application-level function tied largely to TLS and service selection using SNI
The DNS is now used to perform “closest match” service platform selection, supplanting the role of routing
  Most large CDNs run a BGP routing table with an average AS Path Length that is intended to converge to 1!

## Slide 51: Is it Routing? Or Switching?
Let me repeat that, because it’s important:
  Most large CDNs run a BGP routing table with an average AS Path Length that is converging to a value of 1!
The DNS is now used to perform “closest match” service platform selection, supplanting the role of routing
By volume, most of today’s Internet traffic is switched, not routed across the inter-AS space

## Slide 52: It’s Names that drive today’s Internet
TLS is the only underpinning of authenticity in the network
  DNSSEC is largely a market failure
  RPKI really does not matter in a routing-free network!
TLS is a name-based framework for validating authenticity
These days its DNS outages can be globally catastrophic
  While address and routing outages are generally just annoying!
“Evilness” and “DNS abuse” are homonyms these days!

## Slide 53: A new Internet Architecture
We’ve moved from end-to-end peer networks to client/server asymmetric networks
We’ve replaced single platform servers-plus-network to replicated servers-minus-network with CDNs
Clients aren’t identified with a unique public IP address – clients are inside NATs are uniquely identified only in a local context
Individual services aren’t identified with a unique public IP address – services are identified in the DNS

## Slide 54: A new Internet Architecture
We’ve moved from end-to-end peer networks to client/server asymmetric networks
We’ve replaced single platform servers-plus-network to replicated servers-minus-network with CDNs
Clients aren’t identified with a unique public IP address – clients are inside NATs are uniquely identified only in a local context
Individual services aren’t identified with a unique public IP address – services are identified in the DNS
We’ve moved from address-based networks to name-based services

## Slide 55: What am I saying?
The slow uptake of Pv6 is not because this industry is chronically stupid or short sighted
There is something else going on here…

## Slide 56: What am I saying?
IPv6 alone is not critical to a large set of end user service delivery environments
We’ve been able to take a 1980’s address-based architecture and scale it more than a billion-fold by altering the core reliance on distinguisher tokens from addresses to names
  There was no real lasting benefit in trying to leap across to just another 1980’s address-based architecture (with only a few annoyingly stupid differences, apart from longer addresses!)

## Slide 57: Today’s Internet:
Names Matter
The DNS Matters

## Slide 58: Today’s Internet:
Names Matter
The DNS Matters
Addresses - not so much
Address-based Routing - not so much

## Slide 59: Longer Term Trends?
Pushing EVERYTHING out of the network and over to applications
Transmission infrastructure is becoming an abundant commodity
  Network sharing technology (multiplexing) is decreasingly relevant
We have so much network and computing that we no longer have to bring consumers to service delivery points - instead, we are bringing services towards consumers and using the content frameworks to replicate servers and services
With so much computing and storage the application is becoming the service, rather than just a window to a remotely operated service

## Slide 60: Do Networks matter any more?
We have increasingly stripped out network-centric functionality in our search for lower cost, higher speed, and better agility
We are pushing functions out to the edge and ultimately off “the network” altogether and what is left is just dumb pipes?
What defines “the Internet”?
  A common shared transmission fabric, a common suite of protocols and a common protocol address pool?
  or
  A disparate collection of services that share common referential mechanisms using a common name space?

## Slide 61: Some issues to think about
What matters today?
  End Point Addressing – IPv4 / IPv6 / IPv? Absolute? Relative?
    Is universal unique end-point addressing a 1980’s concept whose time has come and gone?
    If network transactions are localised, then what is the residual role of unique global end point addressing for clients or services?
    And if we cannot find a role then why should we bother?
    Who decides when to drop it?
      Is this a market function, so that a network that uses local addressing can operate from an even lower cost base gains a competitive market edge?
      Or are carriage services so cheap already that the relative benefit in discarding the last vestiges of unique global addresses so small that it’s just not worth bothering about?

## Slide 62: Some issues to think about
What matters today?
  Naming and Name Spaces – DNS evolution?
    Are ”names” a common attribute of the network, or an attribute of a service environment or application realm?
    Should names be persistent over time?
    Is the resolution of a name absolute or relative to the content of the resolution query?
    In a world of densely replicated service delivery points how does a client rendezvous with the “best” service point? Does the client work it out? Or the network? Or the service?
    If names are an attribute of applications, then why do we need a single name domain? Surely each application realm can define its own name space? How can we associate a referential name space with a given name?
    If both names and addresses are ephemeral and unstable then what defines the Internet?

## Slide 63: Some issues to think about
What matters today?
  Referential Frameworks?
    Without a common referential space then how do we usefully communicate?
    What do we mean by “common” when we think about referential frameworks?
    How can we join the ‘fuzzy’ human language spaces with the tightly constrained deterministic computer-based symbol spaces?

## Slide 64: Thank You!