## Slide 1: Measuring ECN
Geoff Huston
Chief Scientist, APNIC

## Slide 2: Loss-Based Congestion Control
Most of today’s network traffic uses an extremely simple algorithm that avoids networks collapsing under extreme overload:
  Continually increase the amount of data being pushed into the network
  Until a network queue overloads and the sender detects the consequent packet loss
  Halve the sending rate and do it again!

## Slide 3: Refinements
Change the congestion avoidance inflation algorithm
Try to detect the difference between isolated damage packet loss and queue overload loss
Better understand the relationship between network buffers and protocol performance

## Slide 4: Is there a “better” way?
Trigger the congestion response at the onset of queue formation rather than at the point of catastrophic queue collapse

## Slide 5: BBR
Detect queue formation through pulsed testing and delay sensitivity

## Slide 6: Or get the router to help!
May 1990!

## Slide 7: Or get the router to help!
January 1999!

## Slide 8: Or get the router to help!
January 1999!

## Slide 9: Or get the router to help!
September 2001!

## Slide 10: Then …
Crickets!

## Slide 11: Until around 2022…
L4S!

## Slide 12: ECN Control Loop
A router “marks” IP packets at the onset of queue formation with a bit signal
The Receiver echoes this bit up into the transport protocol reverse flow
The sender reduces its sending window size (and notifies the receiver that it was performed this window reduction)
IP
TCP

## Slide 13: ECN Control Loop
A router “marks” IP packets at the onset of queue formation with a bit signal
The Receiver echoes this bit up into the transport protocol reverse flow
The sender reduces its sending window size (and notifies the receiver that it was performed this window reduction)
IP
TCP

## Slide 14: IP Header
ECN Bits
0 0 – Non-ECN Capable Transport
0 1 – ECN Capable TransporT
1 0 - ECN Capable Transport
1 1 – Congestion Experienced
0 0

## Slide 15: TCP
ECE – receiver back to sender – CE received
CWR – sender to receiver – Congestion Window Reduced
SYN+ECE+CWR – ECN capable on session start
SYN+ACK+ECE – ECN capable response

## Slide 16: ECN Measures
Packet Count (by remote IP addresses) for Feb/March 2025
0. IP Sources 303,545,388
IP ECT 6,815,753 (2.45% of sources)
IP CE 1,098,965 (16.12% of ECT sources)

## Slide 17: ECN Measures
Packet Count (by remote IP addresses)
0. IP Sources 303,545,388
IP ECT 6,815,753 (2.45% of sources)
IP CE 1,098,965 (16.12% of ECT sources)
TCP ECN Opt 7,478,207 (2.46% of sources)
TCP ECE (Rec’d) 20,862 (0.27% of TCP sources)
TCP CWR (Rec’d) 335,209 (4.48% of TCP sources)

## Slide 18: IP ECT by Country

## Slide 19: TCP ECN Option by Country

## Slide 20: Country Table

## Slide 21: Thanks!